Questions for Comment Form for Phase III & IV’s 2nd Posting

- If you have a UVLS program installed to protect the Bulk Electric System, do you have the capability of collecting data to verify that the program operated as intended and to analyze misoperations, including failures to operate?

- Do you agree with the deletion of the following standards from the set of Phase III & IV Standards?

MOD-022 - Use of Disturbance Data to Develop and Maintain Models (Recommend dropping because the requirements are subjective and there aren’t established methods for using disturbance data in models.)

MOD-028 - Provision of Models and Data for Transmission Power Electronic Control Devices (Recommend dropping because the requirements are redundant with MOD-012- Dynamics Data for Transmission System Modeling and Simulation and MOD-013 – Regional Reliability Organization Dynamics Data Requirements and Reporting Procedures.)

PRC-023 - Redundancy of Transmission Protection Systems (Purpose and requirements don’t align with one another.  Recommend remanding to Planning Subcommittee.)

- Do you agree with the proposed definitions that were added or revised?  (misoperation; mitigation plan; protection system)

Misoperation:

- Any failure of a Protection System element to operate within the specified time when a fault or abnormal condition occurs within a zone of protection.

- Any protection system operation for a fault not within a zone of protection (other than operation as backup protection for a fault in an adjacent zone).

- Any operation when no fault or other abnormal condition has occurred.

- Any failure to successfully reclose following a Protection System trip operation.

- Any failure of a generator control system to operate as designed.

- Any unintentional operation when no fault or other abnormal condition has occurred.

Mitigation Plan: A list of corrective actions and an associated timetable for implementation to remedy a specific problem.

Protection System:   Protective relays, associated communication systems, voltage and current sensing devices, power circuit breakers, station batteries and DC control circuitry.

- Please identify anything you believe needs to be modified before this standard is balloted:

EOP-005-1 — System Restoration Plans

- Please identify anything you believe needs to be modified before this standard is balloted:

- MOD-016-1 — Actual and Forecast Demands, Net Energy for Load, Controllable DSM

- Please identify anything you believe needs to be modified before this set of standards is balloted.

MOD-023-1 — Procedures for Validating Generation Equipment Data

MOD-024-1 — Verification of Generator Gross and Net Real Power Capability

MOD-025-1 — Verification of Generator Gross and Net Reactive Power Capability

MOD-026-1 — Verification of Generator Excitation Systems & Voltage Control Model Data

MOD-027-1 — Verification and Status of Generating Unit Frequency Response

- Please identify anything you believe needs to be modified before this set of standards is balloted:

- PRC-018-1 — Disturbance Monitoring Equipment Installation and Data Reporting

- PRC-002-1 — Define and Document Regional Disturbance Monitoring Equipment and Reporting Requirements

- Please identify anything you believe needs to be modified before this set of standards is balloted:

- PRC-003-1 — Regional Procedure for Requirements for Analysis of  Misoperations of Transmission and Generation Protection Systems and Generator Control Systems

- PRC-004-1 — Analysis and Reporting of Transmission and Generation Protection System Misoperations

- PRC-005-1 — Transmission and Generation Protection System Maintenance and Testing

- Please identify anything you believe needs to be modified before this standard is balloted:

- PRC-019-1 — Generator Operation for Maintaining Network Voltage Schedules

- Please identify anything you believe needs to be modified before this set of standards is balloted:

- PRC-020-1 — Under-Voltage Load Shedding Program Database

- PRC-021-1 — Under-Voltage Load Shedding Program Data

- PRC-022-1 — Undervoltage Load Shedding Program Performance

- Please identify anything you believe needs to be modified before this standard is balloted:

- (old VAR-004) PRC-023-1 — Generators Performance during Temporary Frequency and Voltage Excursions

- Please identify anything you believe needs to be modified before this set of standards is balloted:

- VAR-001-1 — Voltage and Reactive Control

- VAR-002-1 — Generator Operation for Maintaining Network Voltage Schedules

- VAR-003-1 — Assessment of Reactive Power Resources

- Please provide any other comments on this set of standards that you haven’t already provided.

- Do you agree with the proposed implementation plan? If no, please identify specifically what you feel needs to be modified.